Checklist for installing AlmaLinux 8.10[1] Server.
[1] This AlmaLinux 8.10 Server from May 31st, 2024 is supported until May 1st, 2029.

Fill in the text box after <...>
<user>	e.g. Karel Zimmer
<username>	e.g. karel
<computername>	e.g. pc01
<user>	i.e. additional users
<username>	i.e. additional users
replace <...> in this checklist with the value in the text box.

Not yet on Linux?	Use Checklist transfer on karelzimmer.nl/en.
New installation?	Start at chapter 2 Perform installation.

Prepare installation

Log in as <user>[2].

Type: wget -O- karelzimmer.nl/getkz | bash
Follow the instructions on the screen.

Type: kz menu
Select 1 Prepare installation.
Follow the instructions on the screen.
[2] Login any additional users and follow the same steps.

Perform installation

Boot the computer from[1] an AlmaLinux 8.10 Server Live[2] USB stick[3].
Select Install AlmaLinux 8.10 and press the Enter key.

Follow the installation screens and complete them.

At WELCOME TO ALMALINUX 8.10 select language and click Continue.

Under USER SETTINGS click User Creation.
Enter your Full name <user>, User name <username>, / check Make this user administrator, / enter a password twice and click Done.

Under SYSTEM click Installation Destination.
Check the Device Selection and click Done.

Under SYSTEM click Netwerk & Host Name.
Move the slider behind the network adapter from OFF to ON.
Enter your Host Name <computername> and click Apply.
Click Done.

Under SOFTWARE click Software Selection.
Select Server and click Done.

Click Begin Installation.

Click Reboot System.
[1] Boot menu/Setup via one of the frequently used keys: Esc, Delete, F1, F2, F9, F10, F11, or F12
[2] From a Live USB stick you can boot and work with AlmaLinux without modifying any files on the hard drive and also allows installation of AlmaLinux.
[3] Create a bootable USB stick: Download a AlmaLinux OS 8.10 DVD ISO from almalinux.org. The next steps are described in Linux information, which can be found at karelzimmer.nl/en.

Finish installation

Log in as <user>.

Type: wget -O- karelzimmer.nl/getkz | bash
Follow the instructions on the screen.

Type: kz menu
Select 3 Finish installation.
Follow the instructions on the screen.

Set up user

Log in as <user>[1].

Go through the welcome screens.

Type: kz menu
Select 4 Set up user.
Follow the instructions on the screen.
[1] Login any additional users and follow the same steps.

End of checklist, AlmaLinux 8.10 Desktop installation is complete.

Written by Karel Zimmer.
License CC0 1.0 .